13VA SERIES 1/3-INCH FORMAT, MANUAL IRIS, VARIFOCAL LENS

TECHNICAL SPECIFICATIONS	SECURITY SYSTEM

DIVISION – LEVEL 1___ 28 ELECTRONIC SAFETY AND SECURITY

LEVEL 2___28 20 00 ELECTRONIC SURVEILLANCE

LEVEL 3___28 23 00 VIDEO SURVEILLANCE

LEVEL 3__28 23 29 VIDEO SURVEILLANCE REMOTE DEVICES AND SENSORS

- GENERAL

    - Equipment and materials used shall be standard components that are manufactured and available for purchase as standard replacement parts as long as the product is commercially available from the manufacturer.

    - All manufactured products shall be thoroughly tested and proven in actual use.

    - All manufactured products shall include, at no additional cost, online support services and availability of a toll-free (U.S. and Canada), 24-hour technical assistance program (TAP) for emergencies.

    - The manufacturer shall repair or replace without charge, manufactured products proven defective in material or workmanship for the stated warranty period from the date of shipment.

- PRODUCTS

  - 1/3-INCH FORMAT, MANUAL IRIS, VARIFOCAL LENS

    - The varifocal lens shall be optimized for maximum light transmission, and it is appropriate for indoor and outdoor lighting situations. The lines shall have excellent low light characteristics.

    - The varifocal lens shall meet or exceed the following design and performance specifications.

      - Physical Specifications

        - Dimensions

          - 13VA1-3:			2.05" L x 1.56" W (5.21 x 3.96 cm)

          - 13VA2.5-6:			1.84" L x 1.56" W (4.67 x 3.96 cm)

          - 13VA2.8-12:			2.33" L x 1.58" W (2.33 x 4.01 cm)

          - 13VA3-8:			2.13" L x 1.51" W (5.41 x 3.83 cm)

          - 13VA5-40:			2.86" L x 1.65" W (7.26 x 4.19 cm)

          - 13VA5-50:			2.33" L x 1.56" W (5.92 x 3.96 cm)

          - 13VA5.5-82.5:			3.25" L x 1.89" W (8.26 x 4.80 cm)

        - Weight

          - 13VA1-3:			0.20 lb (0.09 kg)

          - 13VA2.5-6:			0.20 lb (0.09 kg)

          - 13VA2.8-12:			0.15 lb (0.06 kg)

          - 13VA3-8:			0.09 lb (0.04 kg)

          - 13VA5-40:			0.30 lb (0.14 kg)

          - 13VA5-50:			0.20 lb (0.09 kg)

          - 13VA5.5-82.5:			0.48 lb (0.22 kg)

      - Mechanical Specifications

        - Type:				Varifocal

        - Format Size:			1/3-inch

        - Mount Type:			CS

        - Focal Length

          - 13VA1-3:			1.6~3.4 mm

          - 13VA2.5-6:			2.5~6 mm

          - 13VA2.8-12:			2.8~12 mm

          - 13VA3-8:			3~8 mm

          - 13VA5-40:			5~40 mm

          - 13VA5-50:			5~50 mm

          - 13VA5.5-82.5:			5.5~82.5

        - Zoom Ratio

          - 13VA1-3:			2.1X

          - 13VA2.5-6:			2.4X

          - 13VA2.8-12:			4.3X

          - 13VA3-8:			2.7X

          - 13VA5-40:			8X

          - 13VA5-50:			10X

          - 13VA5.5-82.5:			15X

        - Relative Aperture (F)

          - 13VA1-3:			1.4~Close

          - 13VA2.5-6:			1.4~Close

          - 13VA2.8-12:			1.4~Close

          - 13VA3-8:			1.0~Close

          - 13VA5-40:			1.6~Close

          - 13VA5-50:			1.4~Close

          - 13VA5.5-82.5:			1.8~Close

        - Iris:					Manual

        - Focus:				Manual

        - Zoom:				Manual

        - Diagonal View Angle

          - 13VA1-3:			106.1°~180.0°

          - 13VA2.5-6:			56.8°~133.3°

          - 13VA2.8-12:			N/A

          - 13VA3-8:			44.9°~117.9°

          - 13VA5-40:			8.8°~66.9°

          - 13VA5-50:			N/A

          - 13VA5.5-82.5:			4.2°~64.7°

        - Horizontal View Angle

          - 13VA1-3:			84.3°~180.0°

          - 13VA2.5-6:			45.6°~107.6°

          - 13VA2.8-12:			24.1°~97.4°

          - 13VA3-8:			35.9°~91.0°

          - 13VA5-40:			6.5°~53.6°

          - 13VA5-50:			5.3°~53.4°

          - 13VA5.5-82.5:			3.1°~50.7°

        - Vertical View Angle

          - 13VA1-3:			55.8°~114.1°

          - 13VA2.5-6:			34.2°~80.9°

          - 13VA2.8-12:			18.1°~72.5°

          - 13VA3-8:			26.9°~66.6°

          - 13VA5-40:			4.8°~40.2°

          - 13VA5-50:			4.1°~40.1°

          - 13VA5.5-82.5:			2.3°~37.5°

        - Minimum Object Distance

          - 13VA1-3:			Close

          - 13VA2.5-6:			0.2 m

          - 13VA2.8-12:			0.3 m

          - 13VA3-8:			0.2 m

          - 13VA5-40:			0.5 m

          - 13VA5-50:			0.5 m

          - 13VA5.5-82.5:			0.2 m

        - Back Focal Length

          - 13VA1-3:			7.07~11.55 mm

          - 13VA2.5-6:			8.72~14.24 mm

          - 13VA2.8-12:			8.6 mm

          - 13VA3-8:			8.36~14.12 mm

          - 13VA5-40:			10~14.3 mm

          - 13VA5-50:			10.05 mm

          - 13VA5.5-82.5:			8.65~10.32 mm

        - Filter Size (mm)

          - 13VA1-3:			N/A

          - 13VA2.5-6:			Consult factory

          - 13VA2.8-12:			N/A

          - 13VA3-8:			NIL

          - 13VA5-40:			40.5P0.5

          - 13VA5-50:			N/A

          - 13VA5.5-82.5:			46P0.75

    - Warranty

      - 24 months, parts and labor

    - Pelco Model Numbers

      - 13VA1-3				Varifocal 1.6~3.4 mm lens

      - 13VA2.5-6				Varifocal 2.5~6 mm lens

      - 13VA2.8-12				Varifocal 2.8~12 mm lens

      - 13VA3-8				Varifocal 3~8 mm lens

      - 13VA5-40				Varifocal 5~40 mm lens

      - 13VA5-50				Varifocal 5~50 mm lens

      - 13VA5.5-82.5				Varifocal 5.5~82.5 mm lens