Pelco understands that information is critical to success, which is why we are singularly focused on the development of video surveillance and security solutions that provide you the information necessary to make real-time, business-enabling decisions. From the recently introduced VideoXpert video management platform to our industry-leading selection of IP cameras and accessories, Pelco is committed to designing and delivering a broad range of high-quality, IP video security products and systems complemented with an unparalleled level of customer support and services.

For additional information, contact:

# Pelco

# 625 W. Alluvial Ave.

# Fresno, CA 93711 USA

# Phone: +1 813 888-9555

# Web: www.pelco.com

# E-mail: sales@pelco.com

INDOOR MINI DOME CAMERAS (Spectra Mini SD5 Series)

# DIVISION 28 – ELECTRONIC SAFETY AND SECURITY

28 20 00 	Electronic Surveillance

28 23 00 	Video Surveillance

28 23 29	Video Surveillance Remote Devices and Sensors

Notes to Specifier:

1.  Where several alternative parameters or specifications exist, or where, the specifier has the option of inserting text, such choices are presented in <bold text>.

2.  Explanatory notes and comments are presented in colored text.

INDOOR MINI DOME CAMERAS

- GENERAL

  - SUMMARY

    - Section includes a network dome camera with housing.

## Related Requirements

      - 27 20 00 Data Communications

      - 28 23 13 Video Surveillance Control and Management Systems

      - 28 23 16 Video Surveillance Monitoring and Supervisory Interfaces

      - 28 23 19 Digital Video Recorders and Analog Recording Devices

      - 28 23 23 Video Surveillance Systems Infrastructure

  - REFERENCES

    - Reference Standards

      - Emissions

        - FCC (Class A) - 47 CFR Part 15

        - CE - EN 55022 (Class A), EN 50130-4, EN 60950-1

        - ICES-003, Class A

  - SUBMITTALS

    - Product Data

      - Manufacturer’s printed or electronic data sheets

      - Manufacturer’s installation and operation manuals

      - Warranty documentation

  - QUALIFICATIONS

    - Manufacturer shall have a minimum of five years’ experience in producing analog video equipment.

    - Installers shall be trained and authorized by the Manufacturer to install, integrate, test, and commission the system.

## DELIVERY, STORAGE AND HANDLING

## Deliver the camera in the manufacturer’s original, unopened, undamaged container with identification labels intact.

## Store the camera in a temperature environment protected from mechanical and environmental conditions as designated by the manufacturer.

  - WARRANTY AND SUPPORT

    - Manufacturer shall provide a limited 3-year warranty for the product to be free of defects in material and workmanship.

END OF SECTION

- PRODUCTS

  - EQUIPMENT

    - Manufacturer: 	Pelco

625 W. Alluvial

Fresno, CA 93711 USA

Phone: +1 813 888-9555

Web: www.pelco.com

E-mail: sales@pelco.com

    - Spectra Mini SD5 Series Indoor Mini Dome Cameras:

Model #		Description

SD5-B0		Indoor dome system, black, smoked bubble, NTSC

SD5-B1		Indoor dome system, black, clear bubble, NTSC

SD5-B0-X	Indoor dome system, black, smoked bubble, PAL

SD5-B1-X	Indoor dome system, black, clear bubble, NTSC

SD5-W0	Indoor dome system, white, smoke bubble, NTSC

SD5-W1	Indoor dome system, white, clear bubble, NTSC

SD5-W0-X	Indoor dome system, white, smoked bubble, PAL

SD5-W1-X	Indoor dome system, white, clear bubble, PAL

  - GENERAL DESCRIPTION

    - The indoor CCTV camera dome system shall be a discreet, miniature camera dome system consisting of a dome drive with a variable speed/high speed pan and tilt drive unit with continuous 360( rotation; 1/3-inch CMOS high resolution color camera; motorized zoom lens with optical and digital zoom; auto focus; and an enclosure consisting of a back box, lower dome, and a quick-install mounting.

    - The indoor CCTV camera dome system shall meet or exceed the following design and performance specifications:

      - Vertical Tilt			Unobstructed tilt of +2( to -92(

      - Manual Control Speed:		Pan speed of 0.4( to 80( per second, and pan at 100( per

second in turbo mode. Tilt operation shall range from 0.7( to 40( per second

      - Automatic Preset Speed		Pan speed of 140( and a tilt speed of 80( per second

      - Presets				64 presets. Pan speed of 140( per second and tilt speed at 80(

per second. For variable speed operation an appropriate controller is required.

      - Preset Accuracy		+/- 0.5(

      - Proportional Pan/Tilt Speed	Continually decreases pan and tilt speeds in proportion to the

depth of zoom

      - Automatic Power-Up		User-selectable to the mode of operation the dome will assume

when power is cycled

      - Zones				Four zones with up to 20-character labeling for each, with ability

to blank the video in the zone

      - Motor				Continuous duty, variable speed, operating at 18 to 30 VAC or

25 to 32 VDC

      - Limit Stops			Programmable auto, random and frame scanning

      - Window Blanking		One programmable window blanking area

      - Patterns			One on-screen, programmable pattern including pan, tilt, zoom,

and preset functions; pattern programming through control keyboard following instructions in the on-screen menu.

      - Pattern Length			One pattern of user-defined length, based on dome memory

      - Autosensing			Automatically sense and respond to protocol utilized for

controlling unit whether Coaxitron or RS-422 P or D protocols

      - Menu System			Built-in for setup of programmable functions; multilingual,

including English, French, Italian, Spanish, Portuguese, and German

      - Auto Flip			Rotates dome 180° at bottom of tilt travel

      - Password Protection		Programmable settings with optional password protection

      - Diagnostics			On-screen diagnostic system information

      - Display Setup			User-definable locations of all labels and displays; user-

selectable time duration of each display

      - Azimuth/Elevation/Zoom	On-screen display of pan and tilt locations and zoom ratio

      - RJ45-10 Jack			Pigtail Connector for UTP video, power, and data supplied

      - BNC connector 			Female BNC connector for coaxial video

      - Remote Data Port		Ability to control and setup unit and to upload new operating

code and language file updates through optional remote data port that is located in area with easy access. Compatible with personal computers

      - UTP Compatibility		Unit shall have an unshielded twisted pair circuit for video

transmission up to 750ft

      - Power Consumption		Maximum 21 VA / 15 W

      - Installation/Maintenance		The Spectra Mini’s compact design integrates the “dome drive”

and “top cap” into one comprehensive unit reducing the number of components to make installation and maintenance simple

  - INTEGRATED OPTICS PACKAGE (IOP)

      - Signal Format			NTSC/PAL

      - Scanning System		Progressive

      - Image Sensor			1/3-inch CMOS

      - Effective Pixels			1305 (H) X 1049 (V)

      - Horizontal Resolution		> 700 TVL

      - Minimum Illumination		1.0 Lux

      - White Balance			Automatic with manual override

      - Shutter Speed			Automatic (electronic iris)/manual – 1/60-1/60,000

      - Gain Control			Automatic with manual override

      - Video Output			1.0 to 1.2-volt peak to peak, 75 ohms, adjustable

      - Video Signal-to-Noise		>50 dB

      - Lens				F1.6 (F=5.1-51 mm optical) 10X optical zoom, 8X digital zoom

      - Zoom Speed (optical range)	4.1/2.6/2.1 seconds (menu selectable)

      - Horizontal Angle of View	54° wide zoom, 4.9° telephoto zoom

      - Focus				Automatic with manual override

      - Iris Control			Automatic with manual override

  - ELECTRICAL

    - Input Voltage		25 to 32 VDC, 29 VDC nominal; 18 to 30 VAC, 24 VAC nominal

    - Input Power			21 VA/ 15 W nominal

    - Fuse			1.6 A

    - Connectors:

      - Cable Entry: 		RJ45-10 pigtail connector for video (UTP), power, and data (supplied),

BNC connector for video (coaxial)

      - External power: 	2-conductor power to terminal block

  - TOP CAP AND DOME DRIVE SPECIFICATIONS

    - Construction Material:

      - Top Cap		The top cap shall be manufactured from e-coated cast aluminum and

shall contain heat sink flanges for increased heat dissipation to allow the

dome to be passively cooled

      - Dome Liner		Polycarbonate plastic

      - Trim Ring and Surface

Mount Rings		ABS plastic

      - Bubble			Acrylic

    - Finish:			White or black

    - Light Attenuation

      - Smoked		½ F-stop light loss

      - Clear			Zero light loss

    - Environment		Indoor

    - Unit Weight			1.75 lbs. (0.79 kg)

    - Shipping Weight		4 lb. (1.81 kg)

    - Dimensions 		4.98 in H x 6.19 in W (12.85 cm x 15.72 cm)

    - Temperature:

      - Operating: 		0°C to 50°C (32°F to 122°F)

      - Storage:		-20°C to 60ºC (-4°F to 140ºF)

    - Operating and Storage

Humidity			20% to 80% RH, noncondensing

  - CERTIFICATIONS

    - CE, Class A

    - FCC, Class A

    - UL and cUL Listed

    - ICES-003, Class A

    - RCM

    - ROHS

END OF SECTION

- EXECUTION

  - INSTALLERS

    - Contractor personnel shall comply with all applicable state and local licensing requirements.

## PREPARATION

## The network design and configuration shall be verified for compatibility and performance with the camera(s).

## Network configuration shall be tested and qualified by the Contractor prior to camera installation.

  - INSTALLATION

    - Before permanent installation of the system, the Contractor shall test the system in conditions simulating the final installed environment

      - A report indicating successful test results shall be produced.

## Contractor shall follow all Manufacturer-published guidance on proper installation and configuration of the camera.

  - STORAGE

    - The dome camera hardware shall be stored in an environment where temperature and humidity are in the range specified by the Manufacturer.

END OF SECTION