Pelco understands that information is critical to success, which is why we are singularly focused on the development of video surveillance and security solutions that provide you the information necessary to make real-time, business-enabling decisions. From the recently introduced VideoXpert video management platform to our industry-leading selection of IP cameras and accessories, Pelco is committed to designing and delivering a broad range of high-quality, IP video security products and systems complemented with an unparalleled level of customer support and services.

For additional information, contact:

# Pelco

# 625 W. Alluvial

# Fresno, CA 93711 USA

# Phone: +1 800 289-9100

# Web: www.pelco.com

# E-mail: sales@pelco.com

THERMAL FIXED NETWORK CAMERAS

# DIVISION 28 – ELECTRONIC SAFETY AND SECURITY

28 20 00 	Electronic Surveillance

28 23 00 	Video Surveillance

28 23 29	Video Surveillance Remote Devices and Sensors

Notes to Specifier:

1.  Where several alternative parameters or specifications exist, or where, the specifier has the option of inserting text, such choices are presented in <bold text>.

2.  Explanatory notes and comments are presented in colored text.

THERMAL FIXED NETWORK CAMERAS

- GENERAL

  - SUMMARY

    - Section includes a network thermal fixed camera with housing.

    - Product – A network thermal fixed camera supporting H.264 and MJPEG compression.

## Related Requirements

      - 27 20 00 Data Communications

      - 28 23 13 Video Surveillance Control and Management Systems

      - 28 23 16 Video Surveillance Monitoring and Supervisory Interfaces

      - 28 23 19 Digital Video Recorders and Analog Recording Devices

      - 28 23 23 Video Surveillance Systems Infrastructure

  - REFERENCES

    - Abbreviations

      - AGC - Automatic Gain Control

      - API – Applications Programming Interface

      - ARP – Address Resolution Protocol

      - AWB - Automatic White Balance

      - BLC – Back Light Compensation

      - CBR – Constant Bit Rate

      - CVBR – Constant and Variable Bit Rate

      - DHCP - Dynamic Host Configuration Protocol

      - DNR – Digital Noise Reduction

      - DNS - Domain Name Server

      - EAP – Extensible Authentication Protocol

      - fps - frames per second

      - FTP - File Transfer Protocol

      - GUI – Graphical User Interface

      - HTTP - Hypertext Transfer Protocol

      - HTTPS – Secure Hypertext Transfer Protocol

      - ICMP – Internet Control Message Protocol

      - IGMP - Internet Group Management Protocol

      - IP - Internet Protocol

      - JPEG - Joint Photographic Experts Group

      - LDAP – Lightweight Directory Access Protocol

      - MJPEG - Motion JPEG

      - MPEG - Moving Pictures Experts Group

      - NTP - Network Time Protocol

      - PoE - Power over Ethernet

      - PPPoE - Point-to-Point Protocol over Ethernet

      - QoS – Quality of Service

      - RTP - Real-Time Transport Protocol

      - RTSP - Real-Time Streaming Protocol

      - SMTP - Simple Mail Transfer Protocol

      - SNMP – Simple Network Management Protocol

      - SSH – Secure Shell

      - SSL – Secure Sockets Layer

      - TCP - Transmission Control Protocol

      - UDP - User Datagram Protocol

      - UPnP – Universal Plug and Play

      - VBR – Variable Bit Rate

      - WDR – Wide Dynamic Range

      - VMS - Video Management System

      - WDR – Wide Dynamic Range

    - Reference Standards

      - Network

        - IEEE

          - 802.3 Ethernet Standards

          - 802.1x – Port-based authentication

      - Video

        - ISO / IEC 14496 –10, MPEG-4 Part 10 (ITU H.264)

        - ISO / IEC 10918 – JPEG

        - ONVIF – Profile S, Profile G, and Profile Q

      - Emissions

        - FCC (Class A) – 47 CFR Part 15

        - CE – EN 55022 (Class A), EN 50130-4, EN 60950-1

        - ICES-003, Class A

      - Environmental Models

        - ANSI / IEC 60529 – Degrees of Protection Provided by Enclosures – IP66

        - IK10 (20J) Impact Resistance / IEC62262

        - National Electrical Manufacturers Association, NEMA 250-2003, 4X Enclosure Definition

  - SUBMITTALS

    - Product Data

      - Manufacturer’s printed or electronic data sheets

      - Manufacturer’s installation and operation manuals

      - Warranty documentation

  - QUALIFICATIONS

    - Manufacturer shall have a minimum of five years’ experience in producing IP video equipment.

    - Installers shall be trained and authorized by the Manufacturer to install, integrate, test, and commission the system.

## DELIVERY, STORAGE AND HANDLING

## Deliver the camera in the manufacturer’s original, unopened, undamaged container with identification labels intact.

## Store the camera in a temperature environment protected from mechanical and environmental conditions as designated by the manufacturer.

  - WARRANTY AND SUPPORT

    - Manufacturer shall provide a limited 3-year warranty for the product to be free of defects in material and workmanship.

END OF SECTION

- PRODUCTS

  - EQUIPMENT

    - Manufacturer: 	Pelco

625 W. Alluvial

Fresno, CA 93711 USA

Phone: +1 800 289-99100

Web: www.pelco.com

E-mail: sales@pelco.com

    - Sarix TI Series Thermal Fixed Cameras:

Resolution		FPS	Lens	 Part Number	Description

QVGA (384 x 288)	25 Hz	14 mm	 TI2314		Sarix TI Series Thermal Fixed Camera

QVGA (384 x 288)	25 Hz	35 mm	 TI2335		Sarix TI Series Thermal Fixed Camera

QVGA (384 x 288)	25 Hz	50 mm	 TI2350		Sarix TI Series Thermal Fixed Camera

QVGA (384 x 288)	9 Hz	14 mm	 TI2314-1	Sarix TI Series Thermal Fixed Camera

QVGA (384 x 288)	9 Hz	35 mm	 TI2335-1	Sarix TI Series Thermal Fixed Camera

QVGA (384 x 288)	9 Hz	50 mm	 TI2350-1	Sarix TI Series Thermal Fixed Camera

VGA (640 x 480)	25 Hz	14 mm	 TI2614		Sarix TI Series Thermal Fixed Camera

VGA (640 x 480)	25 Hz	35 mm	 TI2635		Sarix TI Series Thermal Fixed Camera

VGA (640 x 480)	25 Hz	50 mm	 TI2650		Sarix TI Series Thermal Fixed Camera

VGA (640 x 480)	9 Hz	14 mm	 TI2614-1	Sarix TI Series Thermal Fixed Camera

VGA 640 x 480)		9 Hz	35 mm	 TI2635-1	Sarix TI Series Thermal Fixed Camera

VGA (640 x 480)	9 Hz	50 mm	 TI2650-1	Sarix TI Series Thermal Fixed Camera

  - GENERAL DESCRIPTION

    - The network camera system shall offer two simultaneous video streams with either 640 x 480 or 384 x 288 resolution, 17 um.

    - The network camera system shall possess the following primary characteristics:

      - HD visible light and VGA/QVGA thermal channels in one compact unit

      - Advanced thermal optics with 14 mm, 35 mm, and 50 mm lenses available

      - Built-in image processing algorithms and analytics

      - PoE and VDC flexible power options

      - Ruggedly designed to withstand the harshest environmental conditions

      - Easy installation into new and existing infrastructures

      - IP connectivity

      - ONVIF S conformant

      - Full 3-year warranty and support

      - IP66 rated for dust and water ingress protection

      - Uses a standard Web browser for powerful setup and administration

  - CAMERA

    - Imaging Device:

Resolutions

640 x 480, 1024 x 768, or 1280 x 720

    - Imager Type:  ¼-inch color HD CMOS (visual camera), uncooled 17 µ microbolometer 7.5 – 14 µm (thermal camera)

    - Visual Camera

      - Focus:			Autofocus

      - Field of View		52º (H) x 42º (V) @ 102 x 768

      - Signal-to-Noise Ratio:	36 dB

      - Additional Features:	Configurable Resolutions, Digital Zoom

    - Thermal Camera

      - Imager:			17 µ microbolometer 7.5-14 µm

      - Thermal Type:		Uncooled

      - Available Resolutions	VGA, 640 x 480 (TI2614, TI2635, TI2650),

QVGA, 384 x 288 (TI2314, TI2335, TI2350)

      - NETD VGA:		<40º mK, QVGA+: <50º mK

      - Lens Type:		Athermalized, Fixed Focus

      - Frame Rate:		9 or 25 Hz (depending on the model)

      - Digital Zoom:		1x, 2x, 4x

      - Video Modes:		Black hot/white hot

      - Control Operation:	Polarity, NUC, Image Flip, Image Rotation, and Digital Zoom

    - System Interfaces

      - Control: 		ONVIF, web GUI configurator

      - Behaviors		5 Regions of Interest, Directional Filter, 15 User-Defined Virtual Fence,

VMD, Self Scene Learning, Region of Non Interest

      - Field of view:

TI2614		TI2635		TI2650		TI2314		TI2335		TI2350

14 mm		35 mm		50 mm		14 mm		35 mm		50 mm

Diagonal	52.2º		10.7º		15.5º		31.9°		13.3°		9.3°

Horizontal	42.1º		17.7º		12.4º		25.7°		10.7°		7.5°

Vertical		31.9º		13.3º		9.3º		19.4°		8°		5.6°

    - Video:

      - The network camera system shall support up to two simultaneous streams.

      - Video Streams:		Primary H.264, Secondary H.264 and MJPEG

      - Frame Rate:		8.3 Hz or 25 Hz

      - Compression Type:	H.264 and MJPEG

      - Bit Rate Control:	64 kbps – 6 Mbps

      - Streaming:		RTSP, Unicast, Multicast

      - Image Settings:		Brightness, Sharpness, Contrast, Rotation: 0, 90, 180, 270 Horizontal or

Vertical Flip

      - ONVIF S Conformant

    - Minimum System Requirements

      - Operating System:	Windows

      - Network Port:		Standard 10/100 Base-T Ethernet Port

  - ADDITIONAL FEATURES

    - Accessories

      - TICAB-P50		IP/PoE cable. Camera connector terminated on one end, RJ-45 plug on

the other end (15 meter/50-foot length)

    - Recommended Mounts

      - TIWM			Wall mount

      - TIPM			Pole mount adapter (also requires a wall mount)

  - NETWORK

    - Connectivity: 18-pin cable connector. Integration cables should be ordered separately.

    - Protocols supported

      - Internet Protocol (IP) v4

      - Configuration: Dynamic Host Configuration Protocol (DHCP)

      - Web services: Hypertext Transfer Protocol (HTTP), Secure HTTP (HTTPS)

      - Media: Real-Time Streaming Protocol (RTSP)

      - Security: Secure Sockets Layer (SSL), IEEE 802.1x (EAP-TLS)

    - Software Interface: 	Web browser view and setup

  - INTEGRATION

    - The network camera system shall have a built-in web server which supports browser-based configuration.

    - The camera’s web server shall allow access to camera information and all primary software functions.

    - Video Management: 		VideoXpert; VX Toolbox

    - Open API:				Third-party VMS through ONVIF Profile S

    - Camera Discovery:			VX Toolbox

    - Firmware Upgrade:			Web UI or VX Toolbox

    - Web Browser Support:		Yes

  - ELECTRICAL

    - Power Input:			24 VDC Nominal (12 to 32 VDC) or PoE+ (IEEE802.3at)

    - Power Consumption		7 W

    - Alarm Input				Yes

  - MECHANICAL AND ENVIRONMENTAL

    - Construction Material: 		Aluminum

    - Finish:				RAL 9002

    - Dimensions (W x D x H):  		13.45 cm (5.30 in) x 20.2 cm (8.00 in) x 16.9 cm (6.67 in)

    - Temperature:

      - Operating:			-40°C to 55°C (-40°F to 131°F)

      - Operating Humidity:		95%

      - Storage:			-40°C to 71ºC (-40°F to 159.8ºF)

      - Storage Humidity:		95%

    - Ingress Protection:			IP66

    - Weight:				14 and 35 mm, 2.2 kg (4.85 lb)

50 mm, 2.4 kg (5.29 lb)

2.09	CERTIFICATIONS

    - CE (Class A)

    - FCC (Class A)

    - MET

    - IP66

    - ONVIF Profile S

END OF SECTION

- EXECUTION

  - INSTALLERS

    - Contractor personnel shall comply with all applicable state and local licensing requirements.

## PREPARATION

## The network design and configuration shall be verified for compatibility and performance with the camera(s).

## Network configuration shall be tested and qualified by the Contractor prior to camera installation.

  - INSTALLATION

    - Before permanent installation of the system, the Contractor shall test the system in conditions simulating the final installed environment

      - A report indicating successful test results shall be produced.

## Contractor shall follow all Manufacturer-published guidance on proper installation and configuration of the camera.

  - STORAGE

    - The thermal fixed camera hardware shall be stored in an environment where temperature and humidity are in the range specified by the Manufacturer.

END OF SECTION